## Slide 1: VQEG MM Phase 2
Working document towards
a project plan

## Slide 2: Path to MM2 project plan
Target applications / Scope
Subjective testing methodology and set-up
Types of models considered
Data analysis

## Slide 3: Path to MM2 project plan
Target applications
Requires input from industry
will define the range/types of impairments considered in the project
are related to the subjective test methodology
Test methodology and set-up
Discussion based on available data (see proposal for VQEG study)
Types of models
For future discussions
Data analysis
For future discussions

## Slide 4: Path to MM2 project plan
Possible target applications:
  Low-resolution (e.g. mobile streaming or broadcast)
  Standard/high-definition (e.g. satellite/cable broadcasting or IPTV)
  These two families of applications present differences:
    Different format/resolution
    Different range of bit rates
    Different levels of compression impairments
    Different families of audio-video codecs
    May require different subjective test methods

## Slide 5: Subjective test methodology for audio-video quality assessment
Existing Recommendations:
  ITU-R: nothing
  ITU-T: P.911
    Subjective audiovisual quality assessment methods for multimedia applications
    Methods: ACR, DCR, PC and SSCQE
  Issues:
    P.911 does not provide enough clear guidelines on test set-up and offers several test methodologies
    May be out-dated

## Slide 6: Study on subjective audio-video quality assessment: proposal
VQEG runs a series of audio-video subjective experiments
  Produce data that will help deciding which test methodology and test environment set-up should be used for the evaluation of models submitted in the MM2 validation project
  Output of the study will help scientific discussions within MM2 and can be reported to ITU as well
For this study, the same audio-video test material is used to conduct subjective experiments in several labs
Variables can be for example:
  Video presentation device
  Audio presentation device
  Different environment set-up (e.g. audio level normalization)
Participating parties will work on voluntary basis: no fees

## Slide 7: Study on subjective audio-video quality assessment: proposal
Produce a fixed set of audio-video material:
  Need to allow distribution of the material for research purposes
  Same set of material used by all test labs
Results are reported to VQEG
VQEG reports results to ITU

## Slide 8: Study on subjective audio-video quality assessment: proposal
VQEG collaboration project, where any party can help by:
  Providing audio-visual source material (must be able to distribute and use freely for research purposes)
  Proposing test design that can accommodate several test methodologies
  Producing processed audio-video sequences
  Running subjective tests
  Data analysis

## Slide 9: Study on subjective audio-video quality assessment: proposal
Example studies:
  Repeat same test methodology with same room set-up across different labs
  Use different test methodologies with same room set-up in same lab
  Use same test methodology with different room set-ups in same lab

## Slide 10: Study on subjective audio-video quality assessment: proposal
Several studies may be needed (where each study addresses one - or a reduced number - of issues)
This is explorative research and studies do not have to be “perfect”
Main goal of this VQEG study is to bring data on the table to drive the decisions in selecting an adequate test methodology
Other independent studies are welcomed

## Slide 11: Study on subjective audio-video quality assessment: Issues
Problem to run/repeat an audio-video experiment in a lab where participants’ native language differ from language presented in audio track
Audio reference quality required in SRC
Influence of audio presentation device
Influence of audio level presentation (e.g. using or not using audio normalization)
Test design:
  Limited number of combinations of SRCxHRC in a single test
  Choice of low-quality anchors for audio and video
  Well-balanced test exercising enough wide range of audio quality and video quality

## Slide 12: Study on subjective audio-video quality assessment: Issues
Balanced selection of types of audio-video content
  Type of audio content (e.g. music vs. voice-over) may influence perception of errors
Level of expertise of participants:
  Traditionally non-expert subjects are used but maybe expert subjects could provide more stable subjective ratings
  Experts can be people with knowledge of audio-video coding/quality or naïve subjects with extensive practice session before the test
Practice trials:
  Although the subjective test will ask subjects to rate overall quality, should practice trials present only audio-video stimuli?
    Presentation of video-only, audio-only and audio-video stimuli during the practice session may help people focusing on both modalities during the test to provide more stable ratings of overall quality

## Slide 13: Scope of MM2
MM2 will first focus on identification of suitable subjective testing methodology and test set-up/environment
MM2 will focus on audio-video “passive-task” quality assessment, i.e. not interactive experiments
Preliminary studies will use single-stimulus presentation and ACR 5-point scale
Should MM2 subjective tests target only evaluation of overall quality of audio-video stimuli, or target also video-only and audio-only quality?

## Slide 14: List of example studies concerning A/V quality assessment methodology (1)
Expert vs. naïve subjects?
Three quality opinion questions (A, V, AV) in one session or separate sessions?
Audio quality in isolation or audio quality in presence of video (and vice-versa)?
Quality ranges covered by audio and video (e.g., does one modality span a wider range of quality than the other)?
Use of common set of A/V sequences across different tests?
  Common set that contains no spoken audio (i.e., no language issues)

## Slide 15: List of example studies concerning A/V quality assessment methodology (2)
Impact of language & culture
  Issues:
    Speech only, music only, or mixture
    What if subject does not understand the language?
    Can we require test subjects to understand English?
  Options:
    English stimuli with listeners who speak English as a second language; and if so, minimum skill level may be required
    Native English speakers only

## Slide 16: Technical issues in A/V quality assessment
Availability of high-quality audio-video source material that can be used for research purposes (preferably HD resolution)
Listening and viewing environment:
  Headphones or speakers?
  Should test room conform to BS.1116 to control audio characteristics?
  Desire to remove reverberation (etc.) characteristics from test
Impairments: created independently or simultaneously / correlated (e.g., transmission error impacts both audio & video)?
Normalization of audio levels:
  ITU-T Rec. P.56 says how to normalize speech
  No standard exists for normalizing general audio

## Slide 17: Going forward
Who can contribute audio-video source content?
Who can contribute in producing test sequences (i.e. audio-video degraded sequences) assuming availability of source material?
Many different issues to address/investigate in A/V subjective testing set-up => Which aspects/issues should be examined first?
Who can run A/V subjective tests?

## Slide 18: Proposed study
Invitation to participate in a collaborative study focusing on the impact of the test environment:
  Use of an identical set of processed A/V sequences produced by NTIA/ITS
  Use of ACR and 5-point scale
  Repeat the experiment in a pristine sound-proof test room, a quiet but not fully standards-compliant test room (as per ITU-R Rec.) and a noisy environment