## Slide 1: Projected timeline
Timeline
  Selection of SRC (now-Jan)
  Creation of HRC (now-Feb)
  Creation of PVS (Jan-April)
  Collection of Indicators (now-May)
  Objective Quality Metrics (Feb-May)
  Subjective experiments (June-July)
  Analysis (June-September)
  Report (November)
  Dissimination of the Call for Proposals and Participation

## Slide 2: Break-Out
Selection of SRC (now-Jan): Patrik, Glenn, Savvas, Damien
Creation of HRC (now-Feb): Glenn, Mikolaj, Pierre, Chulhee, Damien
Creation of PVS (Jan-April): Chulhee, Margaret, Nicolas, Pierre, Glenn
Collection of Indicators (now-May):
Objective Quality Metrics (Feb-May): Silvio, Chulhee, Margaret
Subjective experiments (June-July)
Analysis (June-September)
Report (November)
Dissimination of the Call for Proposals and Participation

## Slide 3: Task Force: Selection of SRC
Classify SRC into Ivory, Bronze, Silver, Gold
  Objective metrics?
  Subjective evaluation?
Description of the sequence characteristics
Criteria for classification
Task Force Members: Patrik, Glenn, Savvas

## Slide 4: Task Force: Creation of HRCs
Creating VirtualBoxes
Identifying conditions that can be simulated
  JM
  X264
  …
Installation of Ivory chains
Documentation of HRCs
Task Force Members: Glenn, Mikolaj, Pierre, Chulhee

## Slide 5: Output of Ad-Hoc group
Bronze HRC: Codec: - constant bitrate: at least 5 levels - constant rate factor: at least 5 levels = 10 levels in total - GOP: various sizes and structures - # intra frames/ second: at least 2 - # B frames / P frame: at least 2 - hierarchical? 2 , yes, no - slices: at least 2 possibilities: 1 slice or many - encoder parameter for codec?: 2 - fps: 2 levels (normal and 1:2) - spatial resolution: 2 levels Packet loss: - how many packet loss: at least 5 - burstiness: at least 2 levels of burstiness: scattered and burst - random runs of locations of error: at least 2 Decoder: - # decoders: at least 2 Prioritization: 1) random runs of locations of error: at least 2 2) GOP: at least 8 Now: 25600

## Slide 6: Task Force: Creation of PVSs
Allocation of computing power and resources
Getting familiar with running the HRCs
Storing PVSs
Task Force Members: Chulhee, Margaret, Nicolas, Pierre, Glenn

## Slide 7: Task Force: Collection of Indicators
Verification of Model Input/Output
Guiding and supporting proponents for indicators
Computing indicator values if algorithm provided
Checking that the indicator value is available for each PVS
Task Force members:

## Slide 8: Output of Ad-Hoc meeting
A GoogleDoc was created at
https://docs.google.com/spreadsheet/ccc?key=0AlfWKQwnZPhMdE5mcjRUVlhhU3VWSVZ1QmtpdEpIeWc

## Slide 9: Task Force: Objective Quality Metrics
Collection of Full-Reference Video Quality Metrics
Implementation into VirtualBox(es)
Classification and comparison of Metrics
Computing the FR-measures
Analysis of results
Task Force Members: Silvio, Chulhee, Margaret

## Slide 10: Output of ad-hoc meeting
Do editing to SRC and PVS before it reaches objective models
  Length as seen by viewers of subjective test (8 to 10 sec; 15 sec; whatever)
  Durationof SRC used for PCAP file should be considered (this was outside our focus group's scope)
  Uncompressed AVI files, because models can take this file format
  Standard VQEG naming convention from HDTV and MM and RRNRTV is desirable for all SRC and PVS.
  NTIA's models are available already
  All other model owners need JEG to send an official request via email.

## Slide 11: Task Force: Preparation of Subjective Experiments
Choosing Common Set
Dividing PVSs into distinct subjective experiment data sets
Collecting MOS scores from all subjective experiments
Task Force Members:

## Slide 12: Task Force: Analysis
Creation of combination of indicators
Analysis of the performance of indicators
Task Force members:

## Slide 13: Task Force: Dissimination
Investigate, for example, in:
  Liaison statements
  Paper for IEEE Signal Processing
  Distribute the Call on Facebook, LinkedIn, etc.
  Get into contact with IEEE, SPIE etc. for further possibilities
Task Force Members: Patrik, Kjell, Glenn