## Slide 1: MPEG activities

## Slide 2
HEVC: High Efficiency Video Coding
MFC: MPEG Frame Compatible
3DTV

## Slide 3: HEVC
Developed within Joint collaborative Team on Video Coding (JCT-VC) = joint group between MPEG and VCEG
Successor of H.264/AVC
Standardized by Jan 2013
50% bitrate reduction at equal subjective quality
PSNR results:
  All intra: -22% BD-rate
  Random access: -33% BD-rate
  Low delay: -36% BD-rate
1 profile: Main profile
  Up to 8Kx4K @ 120fps
  Lossless support

## Slide 4: MFC
Fit stereoscopic 3D in a 2D picture
  Side-by-side
  Top-bottom

## Slide 5: 3DTV
Main focus is 3D for autostreoscopic displays with compatibility for stereo 3D
  3 texture views + 3 depth views

## Slide 6
Texture+depth summary
Comparison of all five architectures 2 view case:
HP | 0 |  |  |  | 
MVC + tools | -8,27% |  |  |  | 
Hybrid (AVC/HEVC) | -24,83% | -15,97% |  |  | 
MVHEVC | -46,86% | -42,13% | -29,34% |  | 
MVHEVC + tools | -51,42% | -47,21% | -35,48% | -9,14% | 
 | MVC | MVC + tools | Hybrid (AVC/HEVC) | MVHEVC | 
BD-rate gain over