## Slide 1: Proposal to study objective quality assessment of 4K resolution video in the future VQEG tests
Osamu Sugimoto
KDDI R&D Laboratories, Inc.

## Slide 2: Backgrounds
4K video equipment in consumer market
  Monitor
    Toshiba began selling consumer grade 4K TV set in 2011. It supports input of QFHD video signal (3980x2160@60p; without super-resolution) with external 4xHDMI input box.
    Sony announced to launch their first consumer grade 4KTV set in the near future.
  Playback Device
    Some Graphics boards (e.g. AMD FirePro ) have four 1080p outputs and can display 4K/60p resolution on PC.
Storage and Compression
  BDXL: Extended specification of Blu-ray
    Supports 100 and 128GB per one disk
  HEVC video coding
    Better coding efficiency than that of H.264
External QFHD Adapter(~2000USD)
Toshiba 4K2K TV set; (~7000USD)
4K Graphics Board (~1200USD)
4K video will be more popular and industry needs will also increase in the near future

## Slide 3: Proposal
VQEG should include quality assessment of 4K video into the scope of future VQEG tests.
  Subjective test methodologies for large display/screen (50-100inches)
  Objective metrics for quality degradation due to compression coding and transmission
SRC definition
  4K DCI for digital cinema (4096x2160@24fps, progressive)
  4K-QFHD for broadcasting applications (3840x2160@24,25,30,50,60fps, progressive)
HRC to be considered
  H.264
  HEVC
  Intra coding for digital cinema (e.g. JPEG2000) ?

## Slide 4: SRC Availability
NICT 4K/3D contents
  Format: 3840x2160@60fps.
  NTT introduces guidelines to use this test material. ftp://vqeg.its.bldrdoc.gov/Documents/VQEG_Seoul_Jun11/MeetingFiles/3DTV/VQEG_3DTV_2011_015_Distribution of 3D standard contents.doc
SVT High Definition Multi Format Test Set
  Format: 3840x2160@50fps.
  You can download them from the VQEG ftp server. ftp://vqeg.its.bldrdoc.gov/HDTV/SVT_MultiFormat/2160p50_CgrLevels_Master_SVTdec05
  For details, see the following documents. http://svt.se/content/1/c8/02/02/85/31/svt_multiformat_v10.pdf
DCI/STeM
  Maximum resolution of the test sequence is 4096x1714.
  You need to sign the user agreement. http://www.dcimovies.com/StEM

## Slide 5: Subjective test of 4K+HEVC
Test method: DSCQS
Viewing Conditions
  Display: professional 4K projector (JVC)
  Screen size: approx. 190inches
  Viewing Distance: 1.5H (H=screen height)
Number of subjects: 24
Test materials
  14 sequences of 10 sec from KDDI’s own 4K footages
  Format: 3840x2160,30fps, progressive
Coding Condition
  H.264(JM15.1): 8,16,32Mbps (IBBPBBPBBPBBPBB) Rate control enabled
  HEVC(HM6.1) : 4,8,16Mbps (IBBBBBBBBBBBBBB) Fixed QP

## Slide 6: Subjective test of 4K+HEVC
35% of all the HEVC PVSs have better DMOS than those coded by H.264 at twice bitrate.
54% of all the HEVC PVSs have better (smaller) DMOS than those coded by H.264 at the same bitrate.
Chart: Sequence number and Coding Bitrate of HEVC PVSs
| Seq01 04M | Seq03 04M | Seq04 04M | Seq06 04M | Seq09 04M | Seq10 04M | Seq12 04M | Seq16 04M | Seq19 04M | Seq21 04M | Seq23 04M | Seq24 04M | Seq26 04M | Seq27 04M | Seq01 08M | Seq03 08M | Seq04 08M | Seq06 08M | Seq09 08M | Seq10 08M | Seq12 08M | Seq16 08M | Seq19 08M | Seq21 08M | Seq23 08M | Seq24 08M | Seq26 08M | Seq27 08M | Seq01 16M | Seq03 16M | Seq04 16M | Seq06 16M | Seq09 16M | Seq10 16M | Seq12 16M | Seq16 16M | Seq19 16M | Seq21 16M | Seq23 16M | Seq24 16M | Seq26 16M | Seq27 16M
HEVC | 1.4 | 29.6 | 26.7667 | 5.2333 | 16.3333 | 6.1333 | -3.3667 | 2.6333 | 12 | 49.4 | 9.3667 | 8.3333 | 6.2667 | 3.3333 | 3.1333 | 6.5667 | 4.5 | -5.1333 | 10.7 | 3.2333 | -0.33333 | 3.9667 | 1.0333 | 29.1667 | 3.0667 | -3.8333 | 1.6667 | -1.7333 | -8.1667 | 1.6667 | 6.6667 | 5.3667 | 2.4333 | -3.2 | 3.1667 | 2.1 | -8.4667 | 8.2667 | -5.8667 | -3.1 | -2.4667 | 0.4
H.264 | 12.0667 | 7.3667 | 19.0333 | 6.8333 | 20.4 | 7.0333 | 9.0333 | -1.2667 | 8.0333 | 24.0667 | 8.7333 | 6.1 | 4.2 | -3.7333 | -3.0667 | 2.0333 | 1.9667 | -5.1667 | 7.9333 | -3.4 | 9.1 | 13.9667 | -6.7333 | 10.0333 | -0.63333 | 9.9333 | -2.7667 | -2.1667 | 5.4 | 3.7 | -1.5667 | -4.7667 | 1.7333 | -1.7333 | 0.96667 | 1.5667 | -2.7 | -1.8333 | -5.2 | -0.1 | -5.6 | 0.46667

## Slide 7: Conclusion
As 4K will possibly be a part of the mainstream of future video formats, VQEG should begin to study on quality assessment of 4K video.
The HDTV phase2 test seems to be a good opportunity of the first study, but the opportunity is not limited to that. Any other VQEG tests may include 4K into its scope.