## Slide 1: VQEG Rennes meeting june 2012
HDR imaging and video quality
P. Le Callet / M. Perreira Da Silva

## Slide 2: What is HDR ?
Dynamic range is a mix of contrasty and maximum luminance
Current LCD dynamic range
  28 levels but
  max brightness of 500 cd/m2 and 1:1000 max contrast ratio
  this contrast ratio represents only 3 orders of magnitude
Human eyes can adapt from ~10-6 to 106cd/m2 but only 5 orders of magnitude at a time
Aim of HDR imaging : capture and display these 5 orders of magnitude with high fidelity

## Slide 3: HDR capture
Digital camera dynamic rang is 25 to 29
Recent DSLR up to 214 (the limit of 14bits sampling)
For higher dynamic range, multiple images fusion is necessary
  usually multiple exposures are fused
For video, multiple cameras / sensors a used
  Special video rig
+
+
+

## Slide 4: HDR display(s)
Dolby patent
Only one display : sim2 HDR47
  max luminance : up to 4000cd/m2
  max (ANSI) contrast : >20.000:1
  36 bits per pixel
    8 bits per color LCD panel control
    Plus 12 bits leds panel control (2202 individual leds)

## Slide 5: Tone mapping (HDR->LDR)
HDR images cannot be displayed on LDR screens
  Simple contrast reduction is not efficient
  A « tone mapping » operator must be applied
simple contrast reduction
with local tone mapper

## Slide 6: Inverse Tone-mapping (LDR->HDR)
How do we display LDR content on a HDR display ?
  Simple lightness rescaling is not sufficient
  Need for inverse tone-mapping operators

## Slide 7: HDR and quality : new issues
Almost no native HDR capture device
Building HDR content from multiple LDR images causes some defects
  Ghosting in over exposed area
  Alignment / geometrics distortions (HDR rig)
  Lens flares problems between cameras
  Noise due to large difference between the different exposures

## Slide 8: HDR and quality : new issues
Using a HDR display…
  Much higher luminance than usually used in lab experiments
    For LDR content, typical environmental illuminance is 200 lux (ITU-R BT.500)
    How much light is necessary for HDR ?
    Does it have to be dynamically adapted according to the mean luminance of the screen ?
  Need for non normalized experiment rooms ?
  HDR display not easy to feed (for better control LCD panel and backlight data should be addressed separately)
  Almost no HDR video player available
  HDR screen is not transparent : need to be studied
    A « new » technology with its own defects (ex: LEDs bleeding)

## Slide 9: HDR and quality : new issues
HDR displays are not widely available
Using a LDR display for HDR content implies new issues
  Need to apply a tone mapping operator
  Many operators with many parameters
    Hard for find a good set of « universal » parameters
  Tone mapping are not neutral
    Effect on quality and artistic intention
  Most tone mapping operator are built for still images. Big issues with videos because of max luminance changes…

## Slide 10: HDR content transport and coding
How many bits for representing HDR data ?
  What are the effects of quantization ?
Need high bit depth coder
  H.264 is limited to 14 bits
  HEVC ?
Which transport strategy ?
  A single HDR channel ? Multiple LDR ones ?
  LDR fallback possible ?
  Influence on perceived quality

## Slide 11: HDR and QoE
HDR content displayed on HDR display
  Better immersion ?
  More natural images ?
  More emotions conveyed ?
  Visual fatigue due to high luminance ?

## Slide 12: The Nevex Project
French FUI projet
Partners : TF1, Binocle, Transvideo, IRISA, IRCCyN-IVC, Thomson Video Network, Technicolor, Telecom ParisTech, AccepTV, DxO, Polymorph Software
Started in october 2012 – will end in march 2015
Objective : Study and evaluation of a full HDR chain (from capture to display through encoding, transport and decoding)