## Slide 1
glenn.vanwallendael@ugent.be
nicolas.staelens@intec.ugent.be
HEVC in JEG-Hybrid

## Slide 2: SRC selection
10 SRC similar to the AVC experiment within JEG-Hybrid

## Slide 4: HRC
Encoding only
HEVC: HM11.1
Bitrate | 500kbps, 1Mbps, 2Mbps, 4Mbps, 8Mbps, 16Mbps
Rate control | Picture adaptive, CU adaptive
QP | 26, 32, 38, 46
GOP | 1, 2, 4, 8
Intra period | 8, 16, 32, 64
Random access | IDR (closed-GOP intra), CDR (open-GOP intra)
Resolution | 1920x1080, 1280x720, 960x544
Slices | 0, 2, 4, 1500byte

## Slide 5: GOP structures
1:
2:
4:
8:
I
B
B
B
B
I
B
B
B
B
I
B
B
B
B
B
B
B
B
I
B
B
B
B

## Slide 6: PVS generation status
60360 HEVC sequences generated
Corresponds to 292 GB of sequences

## Slide 7: Full-reference metric calculation
In progress:
  Peak Signal-to-Noise Ratio (PSNR)
  Structural Similarity Index (SSIM)
  Video Quality Metric (VQM)
  Visual Information Fidelity (VIF)
Help needed for:
  SwissQual’s Metric
  Tetra Video Quality Metric (TetraVQM)
  MOtion-based Video Integrity Evaluation (MOVIE)

## Slide 8: HMIX generation
Convert bitstream information in XML format
HM 11.1 modified to generate HMIX file
Small differences with JM HMIX
Needs further improvement

## Slide 9: HMIX generation
NAL type
SliceHeader
  SliceType
  POC
  SliceQP
  RPS: RefPOC
CU
  CUQP
PU
  MV
  RefPOC
  IntraDir

## Slide 10: No-reference indicators
Blockiness
Blurriness
Exposure
Noisiness
Flickering
Spatial Activity (Intensity)
Temporal Activity (Intensity)
Spatial Correlation
Energy
Homogeneity
Variance
Contrast
Colour Layout Descriptor
Edge Histogram Descriptor

## Slide 11: Future work
Further encode HEVC PVS
Further calculate full-reference metrics on PVS as ground truth
Start with calculating no-reference indicators on PVS
Create a common AVC-HEVC model based on previously calculated metrics and HMIX information