## Slide 1: AVHD Introduction “Adaptive Streaming Project”

## Slide 2: Target Services
OTT video is currently dominated by:
Netflix
YouTube
Amazon Instant Video
Regarding the introduced distortions, these services should also be representative to others.

## Slide 3: Netflix (2)
On PC Platform:
HTML5 or Silverlight
No DRM-free content available
HTTPS ??
H.264, 235 – 5800 kBit/s
426x240 – 1920x1080 pixel
24 FPS
On Smart TV:
Up to UHD resolution
???
Note: These numbers may be incomplete, content, platform and player depending and change every day!

## Slide 4: Amazon Instant Video (2)
On PC Platform:
HTML5 or Silverlight
DRM-free trailers
HTTPS ??
H.264, 150 – 10000 kBit/s
512x288 – 1920x1080 pixel, 4k ???
24 FPS
On Smart TV:
???
Note: These numbers may be incomplete, content, platform and player depending and change every day!

## Slide 5: YouTube (2)
On PC Platform:
HTML5 or Flash
DRM-free
HTTPS only
H.264, VP9, 70 - 3000 kBit/s
256x144 – 1920x1080 pixel, 4k???
12 – 24 FPS
Note: These numbers may be incomplete, content, platform and player depending and change every day!

## Slide 6: Common Denominator
Protocols: Different DASH-like protocols
Containers: Fragmented MP4 containers
Codecs: H.264, H.265, VP9
Bitrates: 70 kBit/s … 10 Mbit/s
Resolutions: 256x154 pixels.. 1080p
Framerates: 12..24FPS

## Slide 7: Hybrid or not?
Pro Hybrid
Decent accuracy NR models possible
May allow for faster models
Con Hybrid
Developing robust decoders for used containers is time consuming
Developing required DPI modules is time consuming
Will end up in a mess due to high degree of freedom in implementations
Fast changing target
Hybrid project was trivial compared to this case….

## Slide 8: Two Phase Approach
Phase 1: FR, RR, NR Perceptual Models
  Video only (->AV sub project)
  Stalling, bitrate and resolution changes
  H.264, H.265, VP9
  Clipduration at least up to 5 min
Phase 2: Hybrid Models (if required)

## Slide 9: Model Input
Reference signal (SRC):
  Clean signal if available
  Highest available quality on server otherwise
  Always HD
PVS: Degraded signal without stalling
Information on stalling events
  Providing this information separately simplifies the PVS generation.
  Testing the detection of stalling is not the purpose of this project.
  Always HD (upscaled)

## Slide 10: Some more..
Quality changes in the PVS may occur not more than once per second.
Quality changes may include changes of bitrate and/or changes of the video resolution and framerate.
Time frame:
  Test plans ready after next meeting
  Model training should start after this meeting
  Model submission short after the next meeting
  -> We can be really fast -> HDTV Project!