## Slide 1
Marcus Barkowsky Lucjan Janowski Glenn Van Wallendael
VQEG JEG-Hybrid

## Slide 2: Motivation
Collaborative effort on video quality assessment
Research requires knowledge and skills in:
  Subjective evaluation of video quality
  Human visual perception
  Video coding algorithms
  Transmission schemes and network protocols
  Statistical analysis
  Machine learning
  Data mining
Reliable/reproducible/generally applicable results shall be the focus

## Slide 3: Goal
By using a large database covering
    as much as possible sequences
    as much as possible relevant encoder settings
    as much as possible relevant packet loss scenarios
combined with the information delivered from existing full-reference quality metrics
and an as limited as possible subjective evaluation
we try to design a general applicable video quality metric.

## Slide 4: Why a large scale approach?
Analyzing the accuracy of objective measurements with respect to various application scopes. When do specific FR-metrics go wrong?
Identification of insufficient algorithmic modeling precision OR missing perceptual features.
Reproducible verification procedures due to known conditions

## Slide 5: Where to start?
http://vqegjeg.intec.ugent.be/wiki/

## Slide 6: Structure
encode
packet loss
decode
bitstrem indicators
pixel indicators
combination algorithm

## Slide 7: Databases
SRC collection
  4K: more or less 50 4K sequences of 10 sec. (private and public)
For general applicability, do these 4K sequences represent good 4K content?

## Slide 8: Databases and annotation
Coding: H.264, HEVC
12.960 AVC encoded HD video sequences database (10 SRC)
  Objective scores for each sequence: SSIM, PSNR, VQM, PVQM, P.1201.2
59.520 HEVC encoded HD video sequences database (10 SRC)
  Objective scores for each sequence: SSIM, PSNR, VQM, PVQM
40.000 HEVC encoded 4K video sequences database (31 SRC)
MySQL database creation for efficient access of the annotations (main contributor Marcus Barkowsky)

## Slide 9: Packet loss simulation for AVC and HEVC
Robust reference decoder (Enrico Masala)
Advantage: this decoder, by construction, does not cause temporal misalignment between the processed video sequence (PVS) and the original one (SRC).
The decoder gets the original video stream and loss information. Pixels are slice copy concealed, motion information is never lost (not realistic, but robust).
(results: http://media.polito.it/jeg)
HEVC processing tool chain (open source) (Marie-Neige Garcia)
Advantage: realistic simulation

## Slide 10: Objective indicators
Development of pixel based indicators
  Significant contribution from Mikołaj Leszczuk and the MOAVI group
Blockiness, Blur, Exposure time distortion, Interlace, Noise, Framing, Spatial activity, Temporal activity, Flickering, Blackout, Pillarboxing, Letterboxing, Brightness, Contrast, Slicing, Block loss

## Slide 11: Objective indicators
Development of bitstream based indicators
    Significant contribution from Muhammad Shahid
  1 number_of_Cus The number of CUs a slice is divided into
  2 INTRA[%] Percentage of blocks coded as INTRA in a slice
  3 2Nx2N_I[%] Percentage of INTRA coded with partition 2Nx2N in a slice
  4 NxN_I[%] Percentage of INTRA coded with partition NxN in a slice
  5 INTER_P[%] Percentage of blocks coded as INTER P prediction in a slice
  6 INTER_B[%] Percentage of blocks coded as INTER B prediction in a slice
  …
  24 AvgMVx Average value of MV in direction x in a slice
  25 AvgMVy Average value of MV in direction y in a slice
  …
  30 AvgQP Average value of QP in a slice
  31 DevQP Standacrd Deviation of QP in a slice
  32 VarQP Variance of QP in a slice
  …

## Slide 12: Statistical analysis
Statistical analysis of objective Full-Reference measures towards understanding which data needs to be subjectively evaluated
Initial analysis of the data performed:
Mikolaj Leszczuk; Lucjan Janowski; Marcus Barkowsky. Freely Available Large-scale Video Quality Assessment Database in Full-HD Resolution with H.264 Coding, Globecom 2013
Barkowsky, M., Masala, E., Van Wallendael, G., Brunnstrom, K., Staelens, N., & Le Callet, P. (2015). Objective Video Quality Assessment — Towards Large Scale Video Database Enhanced Model Development. IEICE Transactions on Communications, E-98b(1), 2–11.
Van Wallendael, G., Staelens, N., Masala, E., & Barkowsky, M. (2015). FullHD HEVC-Encoded Video Quality Assessment Database. Ninth International Workshop on Video Processing and Quality Metrics (VPQM)

## Slide 13: Combination algorithms
Artificial Neural Network Model
  Inputs: 52 bitstream features of the input Videos
  Hidden layers: 35 sigmoid hidden neurons,
  Output layer: one linear output neuron,
  Output: estimated quality values (estimate FR metrics).
contribution made by Muhammad Shahid

## Slide 14: Organization of reproducible research
A Virtualbox image is updated weekly at:
  ftp://ftp.ivc.polytech.univ-nantes.fr/
  Accessible through TeamViewer (ask credentials to Marcus Barkowsky)
Git repository (software versioning environment)
Identification of HRCs using a MySQL database

## Slide 15: Available toolset
Virtual machine for QoE research including:
  Available encoders (HM, x264, x265)
  Packet loss simulation:
    Robust reference decoder (AVC and HEVC) (Enrico Masala)
    HEVC processing tool chain (open source) (Marie-Neige Garcia)
  Bitstream to machine readable XML
  FR metrics/indicators:
    NR video indicators (MOAVI) (Mikołaj Leszczuk)
    Python implementation of P.1201.2

## Slide 16: 4K content and general applicability
If we build a model around low quality 4K content can we state that a model is generally applicable for 4K then?
Therefore, evaluation of the source content is required:
Berger, K.; Koudota, Y.; Barkowsky, M.; Le Callet, P., "Subjective quality assessment comparing UHD and HD resolution in HEVC transmission chains," in Quality of Multimedia Experience (QoMEX), 2015 Seventh International Workshop on , vol., no., pp.1-6, 26-29 May 2015

## Slide 17: Is 4K content really 4K or HD
Goal: evaluate as much as possible 4K sequences and verify they are of a better subjective quality compared to HD.
Status:
  30 sequences have been evaluated
  Striped (side-by-side) and single stimulus

## Slide 18: Challenge
Development of a NR model distinguishing 4K from HD content.
ICIP 2016 Challenge Session Proposal

## Slide 19: Ongoing work
Biweekly meetings will continue
Quality evaluation of UHD sequences
Further statistics on the large scale database:
  Blind performance estimation of objective measurements
  Determining subset for subjective testing
Further inclusion of objective algorithms (ex. MOAVI)
Running P.1201.2 on the dataset

## Slide 20: Future work
Evaluating performance contribution of individual indicators to more complex algorithms
  in general
  with respect to a specific scope
Development of adapted fusion and machine learning algorithms
Statistical tools for robustness analysis

## Slide 21: Where can I get more information?
http://vqegjeg.intec.ugent.be/wiki/
(notably section resources, constantly updated, volunteers welcome!)
How may I get involved?
Subscribe to the VQEG-JEG mailing list
http://www.its.bldrdoc.gov/vqeg/email-reflectors.aspx
Join our biweekly conference call
(next dates: 28/9 12/10 26/10, 4PM Paris time, reminders and more information sent to JEG mailing list)

## Slide 22
What about collaborations (industry/industry research/industry research/research)?
Collaborations are welcome but financial issues are outside of the scope of this work
What about licenses, patents, etc?
The VQEG-JEG wiki contains a detailed section about this. We are open to patented work but licensing issues are out of scope of our discussions (similar to ITU-ISO/IEC).
What about evaluations of commercial products?
Some companies have offered commercial licenses to some JEG partners for evaluation purposes.