## Slide 1: MOAVI Findings on No-Reference Quality Indicators
Mikołaj Leszczuk, Lucjan Janowski, Jakub Nawała, Michał Zajdel

## Slide 2: Presentation Plan
H.264 quality indicators (update)
H.265 quality indicators (update)
Establishing (selected) perception thresholds (crowdsourcing experiment)
Exploitation (update)
Plans

## Slide 3
H.264 Quality Indicators (Update)

## Slide 4: Signal-Based, NR Indicators for Artefacts of Various Origin
Capturing Artefacts: blurriness, exposure, interlace, etc.
Processing Artefacts: blockiness, blurriness, flickering, reduced spatial & temporal resolution, etc.
Transmission Artefacts: blackout, block loss, freezing, slicing, etc.
Displaying Artefacts: blackout, slicing, etc.

## Slide 5: Merging Exposure and Brightness
Internal similarities of both of metrics
Merged in order to:
  Accommodate for more efficient design of whole application, and
  Better use of available resources
Notes: 3/1/16
5
5

## Slide 6: Exposure Detection (1/2)
Notes: 3/1/16
6
6

## Slide 7: Exposure Detection (2/2)
Merging 3 metrics, namely:
  Blur,
  Contrast, and
  Exposure
Made it possible to detect over- and under-exposure
First tests giving promising results
More precise evaluation is required
Notes: 3/1/16
7
7

## Slide 8: Frame Drop Detection
Possible to detect single/multiple frames drops by analysis of 1st/2nd derivative of Temporal Activity
Functionality currently in development phase
Notes: 3/1/16
8
8

## Slide 9: Overlaying Results onto Video (1/2)
Script merging metrics results with real-time video sequences
Notes: 3/1/16
9
9

## Slide 10: Overlaying Results onto Video (2/2)
Aiding further improvement of metrics’ algorithms
Serving as good tool for:
  Detection of erroneous results, and
  Elimination of erroneous results
Notes: 3/1/16
10
10

## Slide 11: New Noise Metric
Severe instability of previous algorithm
Necessary to introduce brand new code
Based on: “Block-Based Noise Estimation Using Adaptive Gaussian Filtering” (Dong-Hyuk Shin, Rae-Hong Park, Seungjoon Yang, Jae-Han Jung)
Notes: 3/1/16
11
11

## Slide 12
H.265 Quality Indicators (Update)

## Slide 13: New Video Sequences & Scores (1/2)
Notes: 3/1/16
13
13

## Slide 14: New Video Sequences & Scores (2/2)
Got access to new H.265 video sequences & Mean Opinion Scores:
  16 ⨉ 480p
  14 ⨉ 1080p
Source – University of the West of Scotland
Next step – experimenting with new codec
Notes: 3/1/16
14
14

## Slide 15
Establishing Perception Thresholds

## Slide 16: Crowdsourcing Experiment Process Preparation
Objective: set alarm thresholds
Imposed constrains:
  Images, not videos
  8 SRC (reasonable)
W=900 px to fit most displays
51 HRC:
  Blur
  Blockiness
  Contrast
  Noise
408 PVS
9 in common training set

## Slide 17: Crowdsourcing Experiment Interface and Questions

## Slide 18: Crowdsourcing Experiment Subjects
173 subjects:
  Projects
  VQEG
  Social networks
Order:
  Fixed common training set
  Remaining in random
10 scores/picture
Chart: 
| Login only | Common training set only | Usable scores
Subjects | 40 | 42 | 91

## Slide 19: Crowdsourcing Experiment Results (1/2)
Chart: Blockiness level
| 5.0 | 10.0 | 15.0 | 20.0 | 25.0 | 30.0 | 40.0 | 50.0 | 60.0 | 70.0 | 80.0 | 90.0 | 100.0
Mediana | 1 | 1 | 1 | 0.9545 | 0.9028 | 0.775 | 0.6875 | 0.6571 | 0.4286 | 0.3352 | 0.3485 | 0.3167 | 0.3667
Chart: Blur level
| 1.0 | 2.0 | 3.0 | 4.0 | 5.0 | 6.0 | 7.0 | 8.0 | 9.0 | 10.0
Mediana | 0.375 | 0.7 | 0.7273 | 0.8564 | 1 | 1 | 1 | 1 | 1 | 1

## Slide 20: Crowdsourcing Experiment Results (2/2)
Chart: Contrast level
| -80.0 | -70.0 | -60.0 | -50.0 | -40.0 | -30.0 | -20.0 | -10.0 | 0.0 | 10.0 | 20.0 | 30.0 | 40.0 | 50.0 | 60.0 | 70.0 | 80.0
Mediana | 1 | 0.9545 | 1 | 0.9688 | 1 | 0.95 | 0.7639 | 0.4643 | 0.2929 | 0.2946 | 0.5774 | 0.6548 | 0.8875 | 1 | 1 | 1 | 1
Chart: Noise level
| 2.0 | 3.0 | 4.0 | 5.0 | 6.0 | 7.0 | 8.0 | 9.0 | 10.0
Mediana | 0.2727 | 0.48 | 0.4444 | 0.5455 | 0.6364 | 0.875 | 0.8667 | 0.8571 | 0.9091

## Slide 21: Crowdsourcing Experiment Results Analysis
Chart: 
| Blockiness | Blur | Contrast | Noise
Accuracy | 0.7709 | 0.875 | 0.75 | 0.7857

## Slide 22
Exploitation (Update)

## Slide 23: Free A/V Quality Indicators Online at http://vq.kt.agh.edu.pl/

## Slide 24: Maintaining Multi-Platform Binaries Available Online
Goal: to provide up-to-date platform-independent executable
Serving as reference implementation for algorithms developed
To be found at: http://vq.kt.agh.edu.pl/metrics.html
Notes: 3/1/16
24
24

## Slide 25
Plans

## Slide 26: Plans
H.264:
  More precise evaluation of exposure detection
  Development of frame drop detection functionality
  Constant development of overlaying results onto video
H.265:
  Further experimenting with new codec
Funding only until end of September 2016
New idea: standardising quality indicators (spanning beyond funding period)
Discussed commercial exploitation by Net Research