## Slide 1: QAPI: a QoE control technology for online video streaming services
Arifumi Matsumoto
NTT Network Technology Laboratories
VQEG Meeting
2017.5.11

## Slide 2: Who we are
NTT Network Technology Laboratories is in NTT R&D division.
Our team’s research theme: QoE-centric operation
  QoE quantification (standardization)
  QoE measurement/collection
  QoE analysis/visualization
  QoE control
QAPI(Quality API) is an instance of QoE-centric operation

## Slide 3: Even the latest video streaming technology needs improvement
Chart: 
| rebuffering ratio
office | 0.0033
station | 0.025
train | 0.1278
Even with the latest streaming technology, such as ExoPlayer provided by google, video viewing experience is degraded largely due to user mobility and network congestions.
*Rebuffering ratio: the ratio of viewing that includes one or more rebuffering events

## Slide 4: A case with rebuffering
When network quality(throughput) fluctuates, higher bitrates are likely to be chosen mistakenly, which results in rebuffering events at video player.

## Slide 5: QAPI feature#1: Network Quality Prediction
QAPI
server
Congested
area
Non-congested
area
Streaming server
QAPI server predicts and notifies network quality for each viewing.
The user device selects bitrate using the predicted quality.
Network quality
prediction
Network quality
feedback for
future prediction
Bitrate selection based on the prediction

## Slide 6: Rapid Increase of Video Traffic
Video traffic is becoming headaches for carriers/contents providers.
Provisioning/Delivery cost increase, and traffic congestion results in video QoE degradation.

## Slide 7: QAPI feature#2: control balance of QoE and Traffic
Cost(Traffic=bitrate)
QoE
Poor Cost Performance
Cost-Effective
Unacceptable QoE
Target QoE
QAPI enables the control of QoE and Traffic balance.
With the target QoE fixed, QAPI achieves lowest cost delivery, that is, bitrate selection.
QoE model is used for the QoE calculation.
High volume of traffic consumption, but in QoE it makes little difference
QoE rapidly increases as the cost increases

## Slide 8: QAPI core technologies
QoE Model
Network Quality Prediction
Bitrate Selection Strategy
P.NATS model proposed by NTT. This is pluggable.
Based on historical network quality data gathered from user devices.
A series of bitrates is worked out with the QoE targeted, traffic cost lowest.

## Slide 9: QAPI effect: QoE = 4.0 (avg)
Chart: Target QoE = 4.0
| Android | iOS | QAPI
Stop Rate*10 | 1.7 | 0.98 | 0.5
Bitrate | 6.97 | 6.97 | 1.92
QoE | 4.28 | 4.34 | 3.96
With the loss of QoE by 0.3 points, the traffic cost(bitrate) was reduced by 70%.
The strategy with lower stop rate and lower bitrate was chosen to achieve QoE 4.0
This is a simulation result based on real-world data, such as
throughput fluctuation and mobile hand-over occurrences.

## Slide 10: QAPI effect: QoE = 4.0 (CDF)
Target QoE: 4.0
Viewings with QoE > 4.0 are almost zero, viewings with QoE < 4.0 are reduced.
Overall, QoEs are converged to the targeted QoE: 4.0.

## Slide 11: QAPI effect: QoE = 5.0 (avg)
Chart: Target QoE = 5.0
| Android | iOS | QAPI
Stop Rate*10 | 1.7 | 0.98 | 0.39
Bitrate | 6.97 | 6.97 | 9.73
QoE | 4.28 | 4.34 | 4.45
QAPI works for boosting QoE by setting the target QoE 5.0 (maximum).
if the traffic cost(bitrate) increase of 30% is acceptable, QoE can be increased by 0.1, 0.2 points,
This is a simulation result based on real-world data, such as
throughput fluctuation and mobile hand-over occurrences.

## Slide 12: QAPI effect: QoE = 5.0 (CDF)
Target QoE: 5.0
Viewings with QoE < 5.0 are reduced.
The QoE model has the upper limit around 4.5.

## Slide 13: Easy to integrate QAPI into player app.
Streaming server
Quality Prediction
Inside a viewer application
QAPI module
Player GUI
Playlist
Media data
QAPI
server
Quality Feedback
QAPI module is loosely coupled with the player part. The module needs to be called only once for viewing setup.
QAPI module chooses a bitrate and retrieves corresponding media data as guided by the QAPI server.

## Slide 14: Try QAPI !!
QAPI is just baked.
  QAPI is a technology to balance the traffic cost and QoE, and based on network quality prediction.
We are looking for a partner to demonstrate QAPI in the field as a joint effort.
QAPI