## Slide 1: Masked Detection of HEVC Compression Artifacts on Professional, Consumer, and Mobile Displays
Yi Zhang, Yus Yaacob, and Damon M. Chandler Department of Electrical and Electronic Engineering Shizuoka University Hamamatsu, Shizuoka, Japan
Shizuoka
University
静岡大学

## Slide 4: Questions
(1) Can thresholds measured on mobile devices yield the same results as measured on laboratory and desktop displays when viewing conditions and display EOTFs are kept constant?
(2) How are the thresholds affected when EOTFs change on mobile displays, and do such changes agree with model predictions?
(3) How do the variabilities in thresholds due to (1) and (2) compare to the variability across subjects, content, and gaze location?

## Slide 5: Outline
Experiment 1: iPad vs. Others
Experiment 2: iPad “Brightness” settings
Summary
1
2
3

## Slide 6: Experiment 1: Stimuli
Reproducing Thresholds on the iPad

## Slide 7: Experiment 1: Methods
Subjects: Three authors were the subjects
Procedures: Spatial 3AFC, QUEST staircase
7-second time limit, audio feedback
Darkened room (not pitch black, cinema setting)
Displays:
  Cambridge Research Systems Display++ ($10,000)
  I-O Data LCD monitor ($150)
  Apple iPad Air 2 ($650 unit, < $100 LCD+glass alone?)
Viewing distances varied  3×3-deg stimulus
Reproducing Thresholds on the iPad

## Slide 8: Experiment 1: EOTFs
Reproducing Thresholds on the iPad
DataColor Spyder5 ELITE

## Slide 9: Experiment 1: Results
Reproducing Thresholds on the iPad
Chart: Distortion Contrast (dB)
| YY | YZ | DC
Display++ | -34.453 | -29.1708 | -36.6821
I-O Data | -31.3493 | -28.7973 | -32.6173
iPad | -33.5752 | -29.6733 | -36.1363
Shroom
Easier to Detect
Chart: Distortion Contrast (dB)
| YY | YZ | DC
Display++ | -36.4747 | -32.2223 | -36.5947
I-O Data | -35.5535 | -35.062 | -36.9573
iPad | -36.9355 | -32.8095 | -35.1701
SunsetColor
Chart: Distortion Contrast (dB)
| YY | YZ | DC
Display++ | -34.453 | -29.1708 | -36.6821
I-O Data | -31.3493 | -28.7973 | -32.6173
iPad | -33.5752 | -29.6733 | -36.1363
Shroom
Easier to Detect

## Slide 10: Experiment 2: EOTFs
Thresholds on the iPad for different “Brightness” settings
DataColor Spyder5 ELITE
Chart: 8-Bit Digital Pixel Value
| 0 | 20 | 40 | 60 | 80 | 100 | 120 | 140 | 160 | 180 | 200 | 220 | 240 | 255
0% | 0 | 0 | 0.01 | 0.16 | 0.23 | 0.49 | 0.76 | 1.06 | 1.43 | 1.81 | 2.26 | 2.81 | 3.45 | 3.92
50% | 0.19 | 0.69 | 2.03 | 4.93 | 9.81 | 16.87 | 25.82 | 36.25 | 48.33 | 61.39 | 76.3 | 94.48 | 115.49 | 130.74
100% | 0.47 | 1.87 | 5.68 | 13.83 | 27.62 | 47.51 | 72.72 | 101.91 | 135.72 | 172.25 | 213.58 | 264.03 | 321.89 | 363.67
Chart: 8-Bit Digital Pixel Value
| 0 | 20 | 40 | 60 | 80 | 100 | 120 | 140 | 160 | 180 | 200 | 220 | 240 | 255
0% | 0 | 0 | 0.01 | 0.16 | 0.23 | 0.49 | 0.76 | 1.06 | 1.43 | 1.81 | 2.26 | 2.81 | 3.45 | 3.92
50% | 0.19 | 0.69 | 2.03 | 4.93 | 9.81 | 16.87 | 25.82 | 36.25 | 48.33 | 61.39 | 76.3 | 94.48 | 115.49 | 130.74
100% | 0.47 | 1.87 | 5.68 | 13.83 | 27.62 | 47.51 | 72.72 | 101.91 | 135.72 | 172.25 | 213.58 | 264.03 | 321.89 | 363.67
Luminance (cd/m2)

## Slide 11: Experiment 2: EOTFs
Thresholds on the iPad for different “Brightness” settings
DataColor Spyder5 ELITE
Chart: 8-Bit Digital Pixel Value
| 0 | 20 | 40 | 60 | 80 | 100 | 120 | 140 | 160 | 180 | 200 | 220 | 240 | 255
0% | 0 | 0 | 0.01 | 0.16 | 0.23 | 0.49 | 0.76 | 1.06 | 1.43 | 1.81 | 2.26 | 2.81 | 3.45 | 3.92
50% | 0.19 | 0.69 | 2.03 | 4.93 | 9.81 | 16.87 | 25.82 | 36.25 | 48.33 | 61.39 | 76.3 | 94.48 | 115.49 | 130.74
100% | 0.47 | 1.87 | 5.68 | 13.83 | 27.62 | 47.51 | 72.72 | 101.91 | 135.72 | 172.25 | 213.58 | 264.03 | 321.89 | 363.67
50% (daylight) | 2.59 | 3.42 | 5.31 | 8.41 | 14.16 | 21.88 | 30.62 | 40.77 | 51.91 | 64.88 | 78.61 | 95.45 | 115.88 | 130.33
Chart: 8-Bit Digital Pixel Value
| 0 | 20 | 40 | 60 | 80 | 100 | 120 | 140 | 160 | 180 | 200 | 220 | 240 | 255
0% | 0 | 0 | 0.01 | 0.16 | 0.23 | 0.49 | 0.76 | 1.06 | 1.43 | 1.81 | 2.26 | 2.81 | 3.45 | 3.92
50% | 0.19 | 0.69 | 2.03 | 4.93 | 9.81 | 16.87 | 25.82 | 36.25 | 48.33 | 61.39 | 76.3 | 94.48 | 115.49 | 130.74
100% | 0.47 | 1.87 | 5.68 | 13.83 | 27.62 | 47.51 | 72.72 | 101.91 | 135.72 | 172.25 | 213.58 | 264.03 | 321.89 | 363.67
50% (daylight) | 2.59 | 3.42 | 5.31 | 8.41 | 14.16 | 21.88 | 30.62 | 40.77 | 51.91 | 64.88 | 78.61 | 95.45 | 115.88 | 130.33
Luminance (cd/m2)

## Slide 12: Experiment 2: Results
Thresholds on the iPad for different “Brightness” settings
Easier to Detect

## Slide 13: Pilot2 Experiment
Effects of gaze location
SunsetColor
Easier to Detect

## Slide 14: Conclusions
For 8-bit display conditions, thresholds on mobile OK (at least for grayscale still images)
Variations between subjects variations between displays (when matched EOTFs, but also robust to EOTF variations?)
Variations due to local cueing other factors tested here

## Slide 15: Masked Detection of HEVC Compression Artifacts on Professional, Consumer, and Mobile Displays
Yi Zhang, Yus Yaacob, and Damon M. Chandler Department of Electrical and Electronic Engineering Shizuoka University Hamamatsu, Shizuoka, Japan
Shizuoka
University
静岡大学
Thank you very much!