## Slide 1: NTIA/ITS Status Report and Questions
Margaret H. Pinson
mpinson@ntia.doc.gov
+1 303-497-3579

## Slide 2: What Exactly Is Our Goal?
UX / QoE problem?
Acceptable constraints?
NR metric traits?
NR parameters traits?
Dataset design?

## Slide 3: NTIA/ITS Status Report

## Slide 4: No Reference (NR) Metric Goal
Intelligent cameras
Intelligent networks
Quality of experience (QoE)
Notes: “DSLR Camera” © Michele Saad, Intel

## Slide 5: Roadblocks
Accuracy
Industry trust
Suboptimal training datasets
Missing subjective information
  MOS ≠ QoE
  Amateur ≠ professional
  Task

## Slide 6: New Datasets, January 2018
VIME1
  101 photos from VIME photoshoot in Glasgow
CCRIQ2
  4 SRC × 23 cameras
  Extra images from Content Resolution and Image Quality (CCRIQ) Dataset
its4s
  813 unfamiliar video sequences
  Professional videography
  4 sec duration
  32% 720p 24fps, contribution quality
  3% 720p 60fps, contribution quality
  Simple adaptive streaming ladder, 2.34 to 0.5 Mbps

## Slide 7: New Dataset its4s2, in progress
1,444+ images from Flickr
VIME image database
41% public safety
Tablets, 1920 × 1080
Display as 4 sec videos
Consumer cameras
Amateur photography
Lenses
Aspect ratio
Task dependency
Photographic vision
Separate spatial response from temporal response

## Slide 8: New Dataset its4s3, planning
New public safety content
  Crime scene
  Inclement weather
  Drone footage
Professional videographers
Intentionally sloppy technique
HRCs
I want your advice

## Slide 9: Example NR Parameter—Fraction Munsell Red
Why Red?
Characteristic of original content
Not impacted by bitrate, resolution, coding artifacts
Red is “important”
  Photographers, linguists, visual psychologists, anthropologists, …
Very different conventional video or image quality metric
  Blocking, blurring, noise, …
Computation
Color naming system with 7 colors
  Black, grey, white, red, yellow, green & blue
Fraction of red pixels in Munsell color space
  Chroma > 2, hue between 2.5YR and 2.5P
Mean over all frames
Square root

## Slide 10
Video | Original | SRCpls | 2340K | 1732K | 1256K | 0951K | 0512K | Full Dataset
PVS | 0.44 | 0.40 | 0.48 | 0.33 | 0.47 | 0.46 | 0.48 | 0.77
Reference | 0.44 | 0.40 | 0.48 | 0.34 | 0.47 | 0.47 | 0.49 | 0.77

## Slide 11: Dataset Comparison: its4s vs CCRIQ

## Slide 12: What exactly is our goal?

## Slide 13: What Exactly Is Our Goal?
UX / QoE problem?
Acceptable constraints?
NR metric traits?
NR parameters traits?
Dataset design?

## Slide 14: UX / QoE Problem
Intelligent network
  Impact of bandwidth limits on quality
  Priority access
Intelligent camera
  Minimum bandwidth for specific task
  Covert surveillance
  Bodycam
  Remote learning

## Slide 15: Acceptable Constraints—Simplify the Problem
Specify bitrate range per application
Specify amateur vs professional
Specify task
  Entertainment, understand events, recognize people, …
Ignore quality change over time
  Recency effect
Quality as viewed right now
  e.g., ignore potential value of 40 MP image

## Slide 16: Desirable NR Metric Traits
Same metric for images & video
Predict quality of originals
  Real world subject, camera operator, lens, camera electronics, aesthetics, …
Extrapolate “what if”
  Change bitrate, resolution, frame rate, …
Root cause analysis
  Why is the quality bad?
Immediate quality response
  2 frames, ¼ sec, 4 sec

## Slide 17: Desirable NR Parameter Traits
Only respond to one factor
  Upper or lower triangle scatter plot
  Often ignore coding artifacts, resolution, …
Diverse types of factors
  Characterize the scene, operator’s actions, lens, camera, video format, compression, …
Easily explained to naïve user
Computationally simple
Accuracy may depend on quality, task
  More accurate, less accurate, irrelevant
Robust response to new content

## Slide 18: Dataset Design
Unfamiliar SRC
  4 sec, no reuse, no scene cuts
Include bad quality SRC
Training data for specific parameters

## Slide 19: Who is interested? What can you contribute?
NTIA/ITS, subjective datasets