## Slide 1: Broadcast Use Case Discussion
Margaret H. Pinson
mpinson@ntia.doc.gov
Notes: Margaret H Pinson
mpinson@ntia.doc.gov
(+1) 303-497-3579
ITS Institute for Telecommunication Sciences
ITS is the research & engineering branch of the National Telecommunications and Information Administration (NTIA), a part of the U.S. Department of Commerce (DOC). Located at 325 Broadway St., Boulder, CO, USA, 80305. For more information on the ITS Video Quality Research project, see http://www.its.bldrdoc.gov/resources/video-quality-research/video-home.aspx.
“An open exchange of scientific ideas, information, and research achieves the Department’s vision for an informed society that uses objective and factual information to make the best decisions.”—US Department of Commerce Administrative Order DAO 219-1, Public Communications.

## Slide 2: Broadcast NR Metric Capabilities
Key performance indicators (KPI)
  Detect presence
  Confirm absent or not perceptible
Mean Opinion Score (MOS) for operational team, report to management

## Slide 3: Key Performance Indicators (KPI)
Macro-blockiness (e.g. due to too excessive/misconfigured H.26x compression)
Blurriness (e.g. due to too excessive/misconfigured H.26x compression and/or due to video upscaling being applied)
Ringing artifacts (e.g. due to too high compression in JPEG-2000)
Any other visual ‘artifacts’ e.g. caused by RTP packet losses
Motion related artifacts (e.g. caused by low quality de-interlacing, excessive motion blur or camera system misconfiguration)
‘Black frames’, ‘noise frames’ or static video test signal type of content e.g. due to missed/misconfigured sourcing video
Output video framerate is fixed and without any timing variability of (e.g. due to missing or freeze frames)

## Slide 4: Video Content
Mezzanine feeds
  Typically high bitrate
  100MB-200MB for HD
  250MB-500MB for UHD compressed with JPEG2000 or H264
Who can contribute content?
Need a common technical definition

## Slide 5: Video Coding
H.264
  1080p59.94, 422, 10bit
  Fixed GOPsize = 10 - 60 frames range
  Video bitrates range 20 – 60Mbps
JPEG 2000
  720p59.94 – 1080p59.94, 422, 10bit
  Video bitrates range 100 – 200Mbps
Other codecs used in studio environments
  TICO, LLVC, NDI, ProRes
  10-bit depth. 4:2:0, 4:2:2, or 4:4:4 chroma
  Compressed down 2x or 4x for distribution outside the studio