## Slide 1: No-Reference Metrics for Camera Capture: What Should the Scatter Plot Look Like?
Margaret H Pinson
NTIA/ITS
mpinson@ntia.doc.gov

## Slide 2: Questions
Do we trust machine learning?
What does a good NR metric look like? How accurate is good enough?
What constraints can we accept?
  Sub-categories of an application
  Extra specifications & data

## Slide 3: Application
Modern cameras
Carrier-grade network performance
  High throughput
  Very low latency
  Low bit-error rate
Understand quality vs bit-rate
Ignore quality changes over time
Performance degrades gracefully
Video quality & image quality
Definition of “quality” = naïve user
Root cause analysis
  Explain why quality dropped
  MOS splits into multiple factors
  Comprehensible
Goals

## Slide 4: Datasets with Unrepeated Scenes
Its4s
  813 videos, 4 seconds each
  720p 24fps adaptive streaming
  Professional video production
  2.4 to 0.5 Mbps
Its4s2
  1473 images from Flickr
  Some from VQEG VIME
CCRIQ
  392 images
  23 cameras: phone, tablet, compact, DSLR
  16 scene compositions
CCRIQ2 & VIME1
  Thanks to AGH
  92 images extra from CCRIQ
  102 images from VIME in Glasgow
LIVE Public-Domain Subjective in the Wild Image Quality Challenge Database
  1162 images
  500 × 500 pixels
  Phones & tablets

## Slide 5: NR Metrics for IQA with Machine Learning
BRISQUE
  Reported performance: 0.94 Pearson correlation
NIQE
  Reported performance: 0.91 Pearson correlation
OG-IQA
  Reported performance: 0.95 Pearson correlation
  Features: gradient magnitude (GM), relative gradient orientation (RO), relative gradient magnitude (RM)
  Scales 1 and 2
These metrics were NOT intended for the camera capture application

## Slide 6: BRISQUE on Unseen Data
-0.23 Pearson Correlation
-0.50 Pearson Correlation

## Slide 7: NIQE on Unseen Data
-0.32 Pearson Correlation
-0.54 Pearson Correlation

## Slide 8: OG-IQA on Unseen Data
-0.39 Pearson Correlation
-0.63 Pearson Correlation

## Slide 9: BRISQUE, NIQE, OG-IQA

## Slide 10: OG-IQA Features

## Slide 11: ITS NR Feature for Aesthetic Appeal
Munsell red
  Fraction of “red” pixels
Aesthetics, composition, photography, linguistics, color theory, …

## Slide 12: Munsell Red
-0.00 Pearson Correlation
-0.16 Pearson Correlation

## Slide 13: Yes for Professionals — No for Amateurs?
HRC | Correlation
Camera | 0.18
2.34 Mbps | 0.15
1.732 Mbps | 0.28
1.256 Mbps | 0.20
951 Kbps | 0.32
512 Kbps | 0.39

## Slide 14: ITS NR Features
Automatic contrast range
  1% to 99% of luma
Spatial Information (SI) of large objects
  Large objects with sharp edges
  2% of image’s vertical size
  SI energy in top 5% of image
Wiener filter 3×3
  Quality improvement from noise
  Energy of difference, Wiener filtered vs not

## Slide 15: Automatic Contrast Range No for Professionals — Yes for Amateurs?
0.19 Pearson Correlation
-0.02 Pearson Correlation

## Slide 16: Wiener 3x3
0.38 Pearson Correlation
0.17 Pearson Correlation

## Slide 17: Wiener 3x3 — Meaning Changes Across Bit-rate Range
0.38 Pearson Correlation
0.17 Pearson Correlation

## Slide 18: Different Behavior: Camera Capture vs HRC Requires Relative Bit-rate

## Slide 19: “The fitted curves all have the same general shape that demonstrates diminishing returns from increasing the transmission bit rate to the right of the knee.”
"The Relationship Among Video Quality, Screen Resolution, and Bit Rate"
  Gregory W. Cermak; Margaret H. Pinson; Stephen Wolf

## Slide 20: Thank you
Questions
Do we trust machine learning?
What does a good NR metric look like? How accurate is good enough?
What constraints can we accept?
  Sub-categories of an application
  Extra specifications & data
Conclusions
We need more datasets
Flags
  Range of bit-rates for application
  Professional vs amateur
Metadata
  Bit-rate