## Slide 1: Updates on the ITU-T Activities with Respect to Gaming Quality Assessment
Steven Schmidt
Quality and Usability Lab – Berlin Institute of Technology
VQEG Meeting - Seattle, USA, 2020

## Slide 2: What is Cloud Gaming?
Cloud (Server)
Client
Game Input Device
Game
Engine
Video Encoder
Video Decoder
Display
System
Network Characteristic
Bit Rate
Spatial quality (QP)
Temporal quality (Frame Rate)
Player
Latency + Packet Loss
Limited bandwidth
Game
Engine
Ordinary
Online
Gaming
Game
Server
Game
Server

## Slide 3: What are we working on?
User satisfaction for cloud gaming services
  Network provider: network planning / infrastructure
  Service provider: resource distribution
Understanding how to assess gaming QoE and its underlying multidimensional space
Investigating relevant influencing factors on gaming QoE
Predicting gaming QoE

## Slide 4: What is Gaming Quality of Experience?
User
System
Game genre Game structure Game rules
Server Channel Player & device
Experience Playing style Intrinsic motivat.
Static factors Dynamic factors
Context
Physic. & social environment
Extrinsic motivat. Service factors
Influencing
factors
Hedonic Pragmatic
Input quality
Output quality
Interactive behavior
Interaction quality
Novelty
Acceptability
Tension
Learnability
Intuitivity
Immersion
Quality of Experience (QoE)
Appeal
Aesthetics
Playing quality
Positive
affect
Negative
affect
Player experience
Challenge
Competence
Flow
Quality features
[1]

## Slide 5: Standardization Activities
[2]
[3]
[4]
[5]
Creation of 3 work items in ITU-T SG-12
ITU-T Rec. G.1032 (10/2017) – G.QoE-gaming:
  Influence factors on gaming quality of experience
ITU-T Rec. P.809 (05/2018) – P.GAME:
  Subjective evaluation methods for gaming quality
ITU-T Rec. G.1072 (02/2020) – G.OMG:
  Opinion model predicting gaming quality of experience
  for cloud gaming services

## Slide 6: New work items in ITU-T SG-12
P.CROWDG (established during last ITU meeting)
  Subjective evaluation of gaming qual​ity with a crowdsourcing approach
G.OMMOG (established during last ITU meeting)
  Opinion Model for Mobile Online Gaming applications
Propose for next meeting
  Monitoring model predicting gaming quality of experience
  for cloud gaming services
We would be very glad if
you join this activity

## Slide 7: New ITU work item: G.OMMOG
Mobile Online Gaming using interactive multiplayer games
  No offline games or low sensitive games
  Genres: MOBA, Battle Royal, Sport, Shooting
Impairment model structure similar to G.OMG
Influence of Delay (and Jitter) as well as Packet Loss (and bursts)
Combination of 16 network conditions per game
Target group: advanced users but non-professionals
Submission of first draft: April 2020

## Slide 8: Challenges to build Gaming QoE model
Large number of system influence factors
  Encoding and network
  Protocols / error handling
  Devices (displays and inputs)
User factors: casual and pro gamer (target group?)
Strong impact of game content on gaming QoE
Long stimulus duration required: at least 90 seconds for interaction quality
Many quality features to assess (see taxonomy)
Environment: controlled lab vs. home environment

## Slide 9: What do we have / know already
How to assess broad range of quality features more effectively
  Different test paradigms: interactive and passive tests
  How to control for influence factors
Datasets of interactive and passive tests (GPU accelerated encoding)
  Interactive: 12 games using delay, framerate, packet loss, encoding grid points
  Passive: 21 games using bitrate, resolution, framerate, packet loss
Game content must be considered better
Influence of packet loss strongly depends on the implementation of service

## Slide 10: Subjective Test Design for interactive studies
Intro
Stimulus
Rating
Post
15 min
1.5 min
3 min
10 min
1 reference
+ 3 framerates
+ 5 frame loss rates
+ 5 delays
+ 3 bitrates (comparison)
17 conditions
100 minutes
per participant
per game
600 hours for 12 games and 30 participants

## Slide 11: ITU-T Rec. P.809 used for G.1072

## Slide 12: Structure of ITU-T Rec. G.1072

## Slide 13: Quality Impairments used in ITU-T Rec. G.1072
This parameter is valuable for QoE prediction but strongly depends on system => can be monitored

## Slide 14: Impact of game content on model performance (G.1072)
PLCC: 0.82, RMSE: 0.47 PLCC: 0.89, RMSE: 0.33

## Slide 15: Call for New ITU work item
Development of monitoring model for cloud gaming QoE
  Long and short stimuli
  Interactive and passive tests
  Multiple codec, hardware encoding => use of video metrics
  Bitstream header based and payload based => content impact
  Collaborative work item, no patent and no competition
  So far, we received interest from three academic partners, two industrial partners
  Email us if you are interested to join

## Slide 16: Thank you for your Attention!
Updates on the ITU-T Activities with Respect to Gaming Quality Assessment
Steven Schmidt (steven.schmidt@tu-berlin.de)
We are always searching for collaborations 
Visit
www.qu.tu-berlin.de
for more information.

## Slide 17: References
[1] S. Möller, S. Schmidt, and J. Beyer, “Gaming taxonomy: An overview of concepts and evaluation methods for computer gaming qoe,” in Quality of Multimedia Experience (QoMEX), 2013 Fifth International Workshop on, 2013.
[2] S. Möller, S. Schmidt, and S. Zadtootaghaj, “New ITU-T Standards for Gaming QoE Evaluation and Management,” in Quality of Multimedia Experience (QoMEX), 2018 Tenth International Workshop on, 2018.
[3] ITU-T Recommendation G.1032, “Influence factors on gaming quality of experience,” International Telecommunication Union, Geneva, 2017.
[4] ITU-T Recommendation P.809, “Subjective Evaluation Methods for Gaming Quality,” International Telecommunication Union, Geneva, 2018.
[5] ITU-T Recommendation G.1072, “Opinion Model Predicting Gaming QoE for Cloud Gaming Services,” International Telecommunication Union, Geneva, 2020.
[6] F. Schiffner and S. Möller, “Direct Scaling & Quality Prediction for perceptual Video Quality Dimensions,” in 2018 Tenth International Conference on Quality of Multimedia Experience (QoMEX), 2018, pp. 1–3.

## Slide 18: Conditions used to model Interaction Quality
  480p: 1, 2, 4 mbps
  720p: 1, 2, 50 mbps
  1080p: 2, 4, 6, 50 mbps
  Frame Rate: 60, 30, 20, 10 fps
  Frame Loss Rate: 0, 10, 15, 25, 30 %
  Delay: 0, 25, 50, 100, 200, 400 ms
Spatial Video Quality
(blockiness: fragmentation, unclearness)
Temporal Video Quality
(jerkiness: discontinuity)

## Slide 19: Assessed Quality Features
  Overall Quality
  Video Quality (overall and dimensions by Schiffner)
    Fragmentation, Discontinuity, Noisiness, Unclearness, Suboptimal Luminosity
  Audio Quality
  Input Quality: Responsiveness, Controllability, Immediate Feedback
  Player Experience: iGEQ (Immersion, Flow, Tension, Challenge, Competency, positive and negative Affect)
  Performance and Acceptance
    31 items (~3 minutes)
[6]

## Slide 20: Datasets using passive video quality assessment
Three large passive video quality datasets