## Slide 1: No Reference Metric Research Paradigm
Margaret H. Pinson mpinson@ntia.gov

## Slide 2: Prior Work—Limited Scope, No Camera Impairments
Limit scope
  Simplify, few impairments
  External validity problems
  Visual patterns differ
VQEG validation test
  FR, RR, Hybrid, …
  Good quality SRC
Expand scope?
  Not observed
Margaret H. Pinson, "Analysis of No-Reference Metrics for Image and Video Quality of Consumer Applications," NTIA Technical Memo TM-20-547, Jan. 2020
unglamorous,

## Slide 3: NR Metric Design Problems
Current Resources
NORM design specifications
12 datasets
  4,655 images, camera capture
  1,989 videos, camera capture
  3,188 videos, simulated broadcast
NR Metric Framework
Significance test
Diverse researchers
  Unfocused, different applications
Design Challenges
Root cause analysis (RCA)
Incremental improvement
MOS is a function of application
  Simple way to adjust (recipe)
Broad scope
  Camera impairments
  Modern cameras
  Videographer
  Any scene
  Diverse applications

## Slide 4: From RCA to
  wp weight for RCA parameter p
  xp value of RCA parameter p
  number of parameters
Functional programming
Split the research effort by impairment
Ignore impairment: wp = 0
Include
  Image & video
  Camera capture (1st)
  Compression (2nd)
Exclude
  Temporal integration
  Transmission errors

## Slide 5: How to Train RCA?
RCA Challenges
MOS influenced by multiple impairments
Datasets have different impairments
  Type
  Severity
  Relevance  application specific factor
Pearson correlation misleading
RCA Training Strategies Evaluated
Challenge dataset
  Explore one impairment
  Minimize other impairments
Look at scatter plots

## Slide 6
Image Dataset, Camera Capture | Pearson Correlation | False Ranking
BID | 0.50 | 19%
CCRIQ | 0.72 | 12%
CID2013 | 0.75 | 11%
CCRIQ2 & VIME1 | 0.58 | 15%
ITS4S2 | 0.63 | 12%
LIVE-Wild | 0.53 | —
Video Dataset, Camera Capture | Pearson Correlation | False Ranking
ITS4S3 | 0.58 | 15%
ITS4S4 | 0.72 | 11%
KonViD-1K | 0.50 | 15%
Video Dataset, Compression | Pearson Correlation | False Ranking
AGH/NTIA/Dolby | 0.50 | 21%
ITS4S | 0.36 | 21%
vqegHDcuts | 0.26 | 25%
Sawatch Version 2

## Slide 7: RCA Scatter Plot — Scatter Around a Line
RCA Parameter
MOS
0
(min)
1
(max)
1
5

## Slide 8: Fine Detail wp = 0.50
Image Dataset, Camera Capture | Pearson Correlation
BID | 0.38
CCRIQ | 0.53
CID2013 | 0.49
CCRIQ2 & VIME1 | 0.47
ITS4S2 | 0.47
LIVE-Wild | 0.42
Video Dataset, Camera Capture | Pearson Correlation
ITS4S3 | 0.43
ITS4S4 | 0.23
KonViD-1K | 0.42
Video Dataset, Compression | Pearson Correlation
AGH/NTIA/Dolby | 0.27
ITS4S | 0.30
vqegHDcuts | 0.25

## Slide 9: Blur wp = 0.80
Image Dataset, Camera Capture | Pearson Correlation
BID | 0.49
CCRIQ | 0.66
CID2013 | 0.75
CCRIQ2 & VIME1 | 0.49
ITS4S2 | 0.60
LIVE-Wild | 0.50
Video Dataset, Camera Capture | Pearson Correlation
ITS4S3 | 0.50
ITS4S4 | 0.51
KonViD-1K | 0.28
Video Dataset, Compression | Pearson Correlation
AGH/NTIA/Dolby | 0.21
ITS4S | 0.31
vqegHDcuts | 0.01

## Slide 10: RCA Scatter Plot — Lower Triangle
RCA Parameter
MOS
0
(min)
1
(max)
1
5

## Slide 11: White Level wp = 0.25
Image Dataset, Camera Capture | Pearson Correlation
BID | 0.16
CCRIQ | 0.33
CID2013 | 0.48
CCRIQ2 & VIME1 | 0.32
ITS4S2 | 0.20
LIVE-Wild | 0.18
Video Dataset, Camera Capture | Pearson Correlation
ITS4S3 | 0.31
ITS4S4 | 0.02
KonViD-1K | 0.34
Video Dataset, Compression | Pearson Correlation
AGH/NTIA/Dolby | 0.01
ITS4S | 0.00
vqegHDcuts | 0.22
Professional videographers

## Slide 12: Black Level wp = 0.25
Image Dataset, Camera Capture | Pearson Correlation
BID | 0.11
CCRIQ | 0.10
CID2013 | —
CCRIQ2 & VIME1 | —
ITS4S2 | —
LIVE-Wild | 0.07
Video Dataset, Camera Capture | Pearson Correlation
ITS4S3 | —
ITS4S4 | —
KonViD-1K | —
Video Dataset, Compression | Pearson Correlation
AGH/NTIA/Dolby | —
ITS4S | —
vqegHDcuts | —

## Slide 13: Pan Speed wp = 0.70
Image Dataset, Camera Capture | Pearson Correlation
BID | —
CCRIQ | —
CID2013 | —
CCRIQ2 & VIME1 | —
ITS4S2 | —
LIVE-Wild | —
Video Dataset, Camera Capture | Pearson Correlation
ITS4S3 | 0.35
ITS4S4 | 0.79
KonViD-1K | 0.34
Video Dataset, Compression | Pearson Correlation
AGH/NTIA/Dolby | 0.13
ITS4S | 0.10
vqegHDcuts | 0.03
Challenge dataset

## Slide 14: Color Noise wp = 0.35
Image Dataset, Camera Capture | Pearson Correlation
BID | 0.07
CCRIQ | 0.41
CID2013 | 0.49
CCRIQ2 & VIME1 | 0.34
ITS4S2 | 0.26
LIVE-Wild | 0.09
Video Dataset, Camera Capture | Pearson Correlation
ITS4S3 | 0.00
ITS4S4 | 0.01
KonViD-1K | 0.09
Video Dataset, Compression | Pearson Correlation
AGH/NTIA/Dolby | 0.05
ITS4S | 0.25
vqegHDcuts | 0.15

## Slide 15: Blockiness wp = 0.80
Image Dataset, Camera Capture | Pearson Correlation
BID | 0.06
CCRIQ | 0.16
CID2013 | 0.10
CCRIQ2 & VIME1 | 0.25
ITS4S2 | 0.07
LIVE-Wild | 0.15
Video Dataset, Camera Capture | Pearson Correlation
ITS4S3 | 0.45
ITS4S4 | 0.04
KonViD-1K | 0.18
Video Dataset, Compression | Pearson Correlation
AGH/NTIA/Dolby | 0.54
ITS4S | 0.09
vqegHDcuts | 0.44

## Slide 16: Super Saturation wp = 0.05
Image Dataset, Camera Capture | Pearson Correlation
BID | 0.04
CCRIQ | 0.12
CID2013 | 0.09
CCRIQ2 & VIME1 | 0.17
ITS4S2 | 0.05
LIVE-Wild | 0.03
Video Dataset, Camera Capture | Pearson Correlation
ITS4S3 | 0.01
ITS4S4 | 0.14
KonViD-1K | 0.08
Video Dataset, Compression | Pearson Correlation
AGH/NTIA/Dolby | 0.03
ITS4S | 0.03
vqegHDcuts | 0.11

## Slide 17: RCA Scatter Plot — Upper Triangle
RCA Parameter
MOS
0
(min)
1
(max)
1
5

## Slide 18: Pallid wp = 0.05
Image Dataset, Camera Capture | Pearson Correlation
BID | 0.11
CCRIQ | 0.13
CID2013 | 0.00
CCRIQ2 & VIME1 | 0.08
ITS4S2 | 0.24
LIVE-Wild | 0.15
Video Dataset, Camera Capture | Pearson Correlation
ITS4S3 | 0.30
ITS4S4 | 0.15
KonViD-1K | 0.05
Video Dataset, Compression | Pearson Correlation
AGH/NTIA/Dolby | 0.07
ITS4S | 0.22
vqegHDcuts | 0.01
Public safety

## Slide 19: Can You Contribute?
https://github.com/NTIA/NRMetricFramework