## Slide 1: Impact of Spatial and Temporal Information on Video Quality and Compressibility
Werner Robitza1,2, Rakesh Rao Ramachandra Rao2, Steve Göring2, Alexander Raake2
1 AVEQ GmbH, Vienna, Austria
2 Ilmenau University of Technology, Ilmenau, Germany
Video Quality Experts Group — 7-11 June, 2021

## Slide 2: Intro
This presentation is a preview of an upcoming paper at QoMEX 2021
Online from June 14th-17th
https://qomex2021.itec.aau.at/

## Slide 3: Spatial Information / Temporal Information
About SI and TI:
Defined in ITU-T Rec. P.910
Classify spatiotemporal complexity of video sequences
SI: Standard deviation of Sobel-filtered image
TI: A basic motion difference feature for adjacent frames
This contribution:
Related to ongoing VQEG NORM project
SI/TI frequently used for classifying sources for video quality tests
How well can SI/TI be used to gauge compressibility of a video?
By Simpsons contributor, CC BY-SA 3.0, https://commons.wikimedia.org/w/index.php?curid=8904663

## Slide 4: This Contribution
Related to ongoing VQEG NORM project with different activities
  Usage for material with > 8 bit
  HDR
  …
In this contribution, however, focus on:
  SI/TI are frequently used for classifying sources for video quality tests
  Choosing the sources is important for codec development, subjective testing, etc.
How well can SI/TI be used to gauge compressibility of a video?

## Slide 5: Working Hypothesis
Videos with higher SI/TI should be harder to compress
Videos with higher SI/TI have lower quality when compressed under bitrate constraint
High SI/TI lead to lower quality and lower compressibility
Compressibility of a source == achievable quality under bitrate constraints
Quality == subjective or “objective” MOS

## Slide 6: Our Approach
Video database
(AVT-VQDB-UHD1)
Sequences encoded for streaming
(H.264, H.265, VP9)
Source sequences
(Raw UHD-1, 8-10s)
SI/TI
Calculate quality scores and bitrate ladder (MOS, VMAF, ITU-T Rec. P.1204.3)
Compressibility Score
Calculate area under bitrate ladder as compressibility
Determine correlation

## Slide 7: Database and Features
AVT-VQDB-UHD11
Test 1: 180 PVSes
Tests 2 & 3 with overlapping PVSes  mapped into one “virtual” test called “test 2+3” with 320 PVSes
Test 4: includes FPS changes, therefore ignored
SI and TI scores
Per frame, averages, minimum/maximum2
Additionally: Criticality metric from Fenimore et al.3 that uses SI/TI
1 https://github.com/Telecommunication-Telemedia-Assessment/AVT-VQDB-UHD-1
2 calculated via https://github.com/Telecommunication-Telemedia-Assessment/siti-tools
3 see Fenimore et al. (1998), Perceptual Effects of Noise in Digital Video Compression
4 calculated via https://github.com/Telecommunication-Telemedia-Assessment/bitstream_mode3_p1204_3
Video quality scores
Subjective MOS from ITU-T Rec. P.910-compliant lab tests
VMAF (4K model, v0.6.1); full-reference model
ITU-T Rec. P.1204.3; bitstream-based model4

## Slide 8: Data Preparations
Consistency checks:
  “Dancers_8s” contained possibly erroneous PVSes already at encoding stage, and was completely removed
  All VMAF scores for “water_netflix” sequence were erroneous and removed (possible frame offset)
  P.1204.3 scores for four PVSes were removed due to being extreme outliers (possible model bug)
How well do VMAF and P.1204.3 work?
  Very well — see plot on the right
  Pearson correlation between metric and MOS: P.1204.3: 0.96 VMAF: 0.94

## Slide 9: Determining Quality/Compressibility
Create bitrate ladder for each SRC, i.e. MOS against bitrate

## Slide 10: Determining Quality/Compressibility
Create bitrate ladder for each SRC, i.e. MOS against bitrate
Construct convex hull of ideal points

## Slide 11: Determining Quality/Compressibility
Create bitrate ladder for each SRC, i.e. MOS against bitrate
Construct convex hull of ideal points
Fit sigmoid function1 against hull
1 based on: Hanhart et al. (2014), Calculation of average coding efficiency based on subjective quality scores

## Slide 12: Determining Quality/Compressibility
Compressibility
1 number for each SRC/codec combination
Create bitrate ladder for each SRC, i.e. MOS against bitrate
Construct convex hull of ideal points
Fit sigmoid function against hull
Calculate are under each curve as quality/compressibility for that SRC/codec

## Slide 13: Compressibility
Each SRC and codec have different compressibility scores
Note:
Scores are normalized between 0 and 1 for this analysis (to be refined)
Scores are based on MOS here
Examples:
BBB is the easiest to compress, although used very often in tests
Netflix Water sequence is the hardest

## Slide 14: Correlations
TI features have higher correlation with compressibility than SI features
Minimum TI seems like a better correlated indicator than maximum TI
Mean SI correlates better than min/max
Criticality metric from Fenimore et al. has good correlation with compressibility
Features
Correlation with compressibility

## Slide 15: Summary
Method to determine quality/compressibility of a given SRC and codec
  Construct convex hull
  Determine area under the curve
Results:
  SI/TI correlate with quality and compressibility
  Minimum TI is a useful indicator too (for short sequences)
Further research:
  Are there combinations of SI/TI that can be more useful?
  Determine compressibility as a single number on universal scale

## Slide 16: Thank you!