## Slide 1: Datasets for NR Metric Research
Margaret Pinson, mpinson@ntia.gov
Mikołaj Leszczuk, leszczuk@agh.edu.pl
Lukas Krasula lkrasula@netflix.com
Nabajeet Barman n.barman@ieee.org
Maria Martini m.martini@kingston.ac.uk

## Slide 2: Information Format
Media: images or video + duration
Use case: user generated content (UGC) broadcast, medical, first responder, …
Designed for NR metric research: yes or no
Publication: website
Download: website
Experiment design: how the experiment is designed (e.g., rigorous structure, convenience sampling)
Content: type of subject matter, impairments
Other: miscellaneous notes

## Slide 3: Blurred Image Database (BID)
Media: images
Use case: UGC
Designed for NR metric research: yes
Publication: https://ieeexplore.ieee.org/document/5492198
Download: http://www02.smt.ufrj.br/~eduardo/ImageDatabase.htm
Experiment design: Inexact experiment design—photographs chosen from a private collection, one DSLR
Content: diverse subject matter, blur from camera capture

## Slide 4: Consumer Content Resolution and Image Quality Dataset (CCRIQ)
Media: images
Use case: UGC
Designed for NR metric research: no
Publication: https://www.its.bldrdoc.gov/publications/details.aspx?pub=2820
Download: www.cdvl.org
Experiment design: rigorous structure, identical scene compositions photographed with multiple cameras
Content: carefully balanced subject matter
Other:
  Rated on HD and 4K monitors
  Splits nicely by subject matter or camera

## Slide 5: CCRIQ2 & VIME1
Media: images
Use case: UGC
Designed for NR metric research: no
Publication: https://www.its.bldrdoc.gov/publications/details.aspx?pub=3239
Download: www.cdvl.org
Experiment design: exploratory experiment design, similar scene compositions with multiple cameras
Content: VIME1 has cityscapes, CCRIQ2 has carefully balanced content left over from CCRIQ
Other: loose experiment design yielded unreliable MOSs for VIME1

## Slide 6: Camera Image Database 2013 (CID2013)
Media: images
Use case: UGC
Designed for NR metric research: yes
Publication: https://zenodo.org/record/2647033
Download: https://ieeexplore.ieee.org/document/6975172
Experiment design: rigorous structure
Content: limited subject matter, mostly people, identically photographed with multiple cameras
Other: unusual subjective method

## Slide 7: ITS4S2
Media: images
Use case: UGC and first responder (split)
Designed for NR metric research: yes
Publication: https://www.its.bldrdoc.gov/publications/details.aspx?pub=3219
Download: www.cdvl.org
Experiment design: inexact experiment design
Content: diverse camera capture impairments and scene characteristics, diverse subject matter

## Slide 8: LIVE Public-Domain Subjective In the Wild Image Quality Challenge Database (LIVE-Wild)
Media: images
Use case: UGC
Designed for NR metric research: yes
Publication: http://live.ece.utexas.edu/research/ChallengeDB/index.html
Download: http://live.ece.utexas.edu/research/ChallengeDB/index.html
Experiment design: inexact experiment design
Content: mobile phone devices and camera capture impairments, diverse subject matter
Other: (500 x 500) pixels

## Slide 9: ITS4S3
Media: video, 4 seconds
Use case: first responder
Designed for NR metric research: yes
Publication: https://www.its.bldrdoc.gov/publications/details.aspx?pub=3220
Download: www.cdvl.org
Experiment design: exploratory experiment design
Content: professional videographers recreate common camera capture problems for the first responder use case

## Slide 10: ITS4S4
Media: video, 4 second
Use case: UGC and first responder (mixed)
Designed for NR metric research: yes
Publication: https://www.its.bldrdoc.gov/publications/details.aspx?pub=3233
Download: www.cdvl.org
Experiment design: exploratory experiment design,
Content: pans from professional footage, plus simulated pans created from high resolution images
Other: proof of concept for RCA metric training method

## Slide 11: KoNViD-1K
Media: video, 8 seconds
Use case: UGC
Designed for NR metric research: yes
Publication: http://database.mmsp-kn.de/
Download: http://database.mmsp-kn.de/konvid-1k-database.html
Experiment design: rigorous structure, objective video selection criteria
Content: diverse subject matter, camera capture impairments
Other: sub-optimal for NR metric research
  Videos contain temporal changes in quality
  Filmed 2004 to 2014, lower quality than contemporary cameras

## Slide 12: ITS4S
Media: video, 4 seconds
Use case: adaptive streaming, 83% entertainment, 16% first responder
Designed for NR metric research: yes
Publication: https://www.its.bldrdoc.gov/publications/details.aspx?pub=3194
Download: www.cdvl.org
Experiment design: rigorous structure, unrepeated scene experiment design
Content: video from professional videographers
Other:
  Occasional low-quality video that professionals would discard
  Splits nicely by bitrate
  Main ratings from ITS
  Additional ratings from FOWR/ITERO dataset
  Additional ratings from AGH

## Slide 13: AGH/NTIA/Dolby
Media: video, 8 second
Use case: broadcast
Designed for NR metric research: no
Publication: https://link.springer.com/article/10.1007/s41233-019-0026-4
Download: www.cdvl.org
Experiment design: rigorous structure, partially unrepeated scene experiment design
Content: mix of MPEG2, H.264, H.265 compression, diverse subject matter
Other: temporal changes in quality

## Slide 14: vqegHDcuts
Media: video, 1 to 8 seconds
Use case: broadcast
Designed for NR metric research: no
Publication: https://www.its.bldrdoc.gov/publications/details.aspx?pub=3235
Download: www.cdvl.org
Experiment design:
  Faux dataset created from VQEG HDTV tests
  Each sequence cut whenever the content or camera motion changed
  MOS of the entire sequence assigned to each segment
  Videos with transmission errors omitted
Content: professional videographer, various compression
Other: exploratory technique for creating dataset for NR metric research

## Slide 15: Parking Database
Media: video, 20 seconds
Use case: first responder
Designed for NR metric research: yes
Publication: “Quality assessment for a license plate recognition task based on a video streamed in limited networking conditions,” International Conference on Multimedia Communications, Services and Security, pp. 10–18, Springer, Berlin, Heidelberg 2011.
Download: https://qoe.agh.edu.pl/parking-database/
Experiment design:
  source video sequences collected at a car parking lot of AGH University of Science and Technology
  videos recorded by a parking lot CCTV camera during high traﬃc volume
  the camera located 50 meters from the parking lot entrance in order to simulate typical video recordings
  adjusted the video compression parameters in order to cover the recognition ability threshold
Content: type of subject matter, impairments
Other: one can also download the ground truth (vehicle registration plate) file for each video sequence as well as the subjective scores file

## Slide 16: SYNAT database
Media: video, 10 seconds
Use case: broadcast and internet streaming
Designed for NR metric research: no
Publication: “Freely available large-scale video quality assessment database in full-HD resolution with h. 264 coding,” 2013 IEEE GLOBECOM Workshops (GC Workshops), pp. 1162–1167, IEEE 2013.
Download: https://qoe.agh.edu.pl/synat-database/
Experiment design:
  the database comprising JM/x264-encoded video sequences
  An extensive possible encoding parameter space selection of 1296 configurations
  some Full-Reference (FR) and No-Reference (NR) metrics were selected and calculated
Content: type of subject matter, impairments
Other: one can download for free results of this work stored as a file *.mat and video sequences stored in 10 folders containing about 13 000 video samples produced during the test

## Slide 17: Sharpened Images Database (SID)
Media: Images
Use case: image sharpening
Designed for NR metric research: yes
Publication: Krasula, L., Le Callet, P., Fliegel, K, Klíma, M. “Quality Assessment of Sharpened Images: Challenges, Methodology, and Objective Metrics,” IEEE Transactions on Image Processing, vol. 26, no. 3, pp. 1496 - 1508, 2017.
Download: https://drive.google.com/file/d/1btjT0QFPfNKTcZyxM8Neqz01eTt_6cX3/view
Experiment design: rigorous structure
  144 images in total = 4 SRCs x 36 HRCs
  Original + 3 degrees of blur + 4 sharpening methods x 8 parameters settings
Content: A database with blurred, sharpened, and over-sharpened images evaluated together
Other:
  Pair comparison
  Resolution 512x512

## Slide 18: Tone-Mapped Image Quality Database (TMIQD)
Media: Image
Use case: HDR, tone-mapping
Designed for NR metric research: yes
Publication: Krasula, L., Narwaria, M., Fliegel, K., Le Callet, P. “Preference of Experience in Image Tone-Mapping: Dataset and Framework for Objective Measures Comparison,” IEEE Journal of Selected Topics in Signal Processing, vol. 11, no. 1, pp. 64 - 74, 2017.
Download: https://drive.google.com/file/d/0B7jKyX6oxhG3OUs4OHA5MFRMVWs/view?resourcekey=0-ZHMdz5_I-iSWVWDFZNOpDg
Experiment design: rigorous structure
  80 images in total - 20 SRCs (10 natural & 10 synthetic) x 9 HRCs
  4 TMOs * 2 parameters settings + 1 TMO without parameters
Content:
  A database of both natural and synthetic HDR images tone-mapped into SDR using different tone-mapping operators
  Image tone-mapping introduces specific artifacts in both luma and chroma most of the objective metrics cannot reliably capture
  Resolution 1920 x 1080

## Slide 19: Youku video database with 1072 UGC/PGC/OGC video sequences (Youku-V1K)
Media: video, 10 seconds
Use case: online video hosting platform
  User generated content (UGC)
  Professionally generated content (PGC)
  Occupationally generated content (OGC)
Designed for NR metric research: yes
Publication: Jiahua Xu, Jing Li, et.al, "Perceptual Quality Assessment of Internet Videos", ACM MM 2021,
Download: https://jingnantes.github.io/acmmm21-youku-v1k/
Experiment design: rigorous structure, objective content sampling strategy
Content: videos from the Youku video hosting platform, China
Other:

## Slide 20: GamingVideoSet
Media: video, 30 s, 1080p 30fps, SDR
Use case: gaming video streaming
Designed for NR metric research: yes
Publication: https://ieeexplore.ieee.org/abstract/document/8463362
Download Videos: https://kingston.box.com/v/GamingVideoSET request password from authors
Download individual subjective scores: https://ieeexplore.ieee.org/abstract/document/9154548
Experiment design: Convenience sampling
Content:
  24 videos
  Subjective results available for 6 videos. ACR
Authors:
  Nabajeet Barman, n.barman@ieee.org,
  Maria Martini, m.martini@kingston.ac.uk

## Slide 21: KUGVD
Media: video, 30 s, 1080p 30fps, SDR
Use case: gaming video streaming
Designed for NR metric research: yes
Publication: https://ieeexplore.ieee.org/document/8727887
Download: https://kingston.box.com/v/KUGVD
  Request password from the authors.
Experiment design: convenience sampling
Content:
  24 videos
  Subjective results for 6 videos, ACR
Other: Designed in line with GamingVideoSET dataset. Individual subjective scores available
Authors:
  Nabajeet Barman, n.barman@ieee.org,
  Maria Martini, m.martini@kingston.ac.uk

## Slide 22: GamingHDRVideoSet
Media: video, 10 s, 4K 30fps, HDR, BT.2020 NCL, PQ
Use case: HDR gaming video streaming
Designed for NR metric research: yes
Publication: https://ieeexplore.ieee.org/abstract/document/9422736
Download: https://github.com/NabajeetBarman/GamingHDRVideoSET
Experiment design: convenience sampling
Content: subjective tests in progress; should be ready by VQEG meeting (ACR-HR)
Other: currently the dataset is available on a request only basis
Authors:
  Nabajeet Barman, n.barman@ieee.org,
  Maria Martini, m.martini@kingston.ac.uk

## Slide 23: YouTube UGC Dataset (YT-UGC)
Media: video
Use case: UGC
Designed for NR metric research: Yes
Publication:
  Balu Adsumilli et al., "Launching a YouTube dataset of user-generated content", YouTube tech blog
  Yilin Wang et al., "YouTube UGC Dataset for Video Compression Research", MMSP 2019
  Joong Yim et al., "Subjective Quality Assessment for YouTube UGC Dataset", ICIP 2020
  Yilin Wang et al., "Rich features for perceptual quality assessment of UGC videos", CVPR 2021
Download: media.withyoutube.com
Experiment design:
  YT-UGC dataset contains 1500 20s clips sourced from 1.5 millions YouTube uploads.
  We sampled videos based on their spatial/temporal/color complexity and chunk variations, so the dataset has a good coverage of current YouTube corpus.
  We collected MOS (via MTurk) for all videos, and DMOS for popular content categories like Gaming and Sports.
  The dataset also provides 600+ content labels which enables exploring the connection between video content and perceptual quality.

## Slide 24: AVT-VQDB-UHD-1 database
Media: videos
Publication: https://ieeexplore.ieee.org/document/8959059
Download: https://github.com/Telecommunication-Telemedia-Assessment/AVT-VQDB-UHD-1
Experiment design: conventional
Other: dataset consists of 4 different tests

## Slide 25: Medical Ultrasound Images (Original+ Denoised) Database: MUI2018
Media: image
Use case: medical
Designed for NR metric research: yes
Publication: https://iopscience.iop.org/article/10.1088/1361-6560/aadbc9/pdf
Download:
https://drive1.demo.renater.fr/index.php/s/jFR5J6j3fWFAet4
Experiment design: Exploratory experiment design
Content: SAMVIQ protocol, 3 radiologists, reference images with 5 denoising algorithms, four criteria assessed (Diagnostic, Textures, Edges, Contrast).

## Slide 26: LVQ database 2020
Media: video
Use case: medical
Designed for NR metric research: Yes
Publication: https://arxiv.org/pdf/2003.12679.pdf
Download: https://drive.google.com/file/d/1SoONeacp9vvihTY7zmWssG_cnVzx16oq/view
Experiment design: Exploratory experiment design
Content: Pairwise-comparison protocol, thirty non-expert and ten expert observers, a database of 2D laparoscopic videos (LVQ), by simulating five common distortions affecting a laparoscopic video (smoke, noise, uneven illumination, blur due to defocus, blur due to motion) identified in close cooperation with medical experts.
Other: The experience years of each expert are not clear.

## Slide 27: Discussion — Seeking Other Datasets — Which Are Best?
IQA UGC
  Fast to compute NR metrics
VQA UGC
  Videos that do not require temporal integration (4 second)
  Slightly longer videos with temporal changes (8 to 15 seconds?)
VQA for Broadcast applications
  High industry interest, based on NORM discussions
  Poor availability 
Other use cases
  Computer vision, medical, gaming, …